Curves and Surfaces

---
Curves and Surfaces
- Need for Parametric Equations
- Affine Combinations
- Bernstein Polynomials
- Bezier Curves and Surfaces
- Continuity when joining curves
- B Spline Curves and Surfaces

---
Need for Parametric Equations
- Traditionally we’ve been using functions of the form y = f(x), good to illustrate mathematical concepts but are restrictive.
- Restrictive in the sense we can have only one value of y for each value of x. (not good for representing curves)
- Parametric curves are defined using a parameter ‘t’ and have defining function for each of the coordinate for a certain point
  x = f(t)
  y = g(t)
  where t is usually restricted to an interval t:[a;b]
- Frequently a parametric curve is written as (x(t),y(t)), emphasizing the two functions that define the curve, or is written P(t), where P is a two-dimensional point .

---
Need for Parametric Equations
For parametric representations of surfaces, we use two parameters, say u and v , and represent the surface as
x = f ( u,v )
y = g ( u,v )
z = h ( u,v )
for some functions f , g , and h , and where u and v are contained in some intervals, u:[a;b],
v:[c;d]

---
Parametric equation for a Line
- Given two points P0 = (x0,y0) and P1 = (x1,y1) we can form a straight line by
  (x,y) = (1-t).(x0,yo) + t.(x1,y1)
  = ((1-t).x0 + t.x1, (1-t).y0 + t.y1)
  Where t [0,1]
  Here,
  f(t) = (1-t).x0 + t.x1
  g(t) = (1-t).y0 + t.y1 in the definition above.
- We can also write the above line as
  P(t) = (1-t)P0 + t.P1

---
Affine Combination
- In mathematics, a linear combination of vectors x1, ..., xn
  is called an affine combination of x1, ..., xn when the sum of the coefficients is 1, that is,
- In case of our line defined on the previous page,
  P(t) = (1-t) P0 + tP1 is an affine combination with
  a1 = (1-t) and a2 = t, and a1 + a2 yields in 1.
`

---
Convex Combinations
- Given a set of points P0,P1, …Pn, we can form affine combinations of those points by selecting a0,a1,….an with a0 + a1 + .. + an = 1 and form new points
  P = a0P0 + a1P1 + … + anPn
  If each ai is such that 0 <= ai <= 1, then each generated point P is called a convex combination of the points P0,P1,…, Pn
- Given any set of points, we say that the set is convex , if given any two points of the set, any convex combination of these two points is also in the set.

---
Convex Hull
The set of all points P that can be written as convex combinations of P0,P1,.., Pn is called the convex hull of the points P0,P1, .., Pn. The convex hull is the smallest convex set that contains all the set of points P0, P1, .., Pn

---
Bernstein Polynomials
- The Bernstein Polynomial of degree n are defined by
  for i=0,1,…..n, where
- There are n+1 nth-degree Bernstein polynomials. And if i<0 or i>n Bi,n=0
Bernstein Polynomials of degree 1	Bernstein Polynomials of degree 2
B0,1 = 1-t B1,1 = t	B0,2 = (1-t)2 B1,2 = 2t(1-t) B2,2 = t2

---
Bezier Curve
- To define a Bezier Curve of degree n we need a set of n+1 (P0,P1,..,Pn) control points.
- The points P0 and Pn are the extremities of the curve, none of the other points fall on the curve, but they act as points of attraction for the curve.
- The degree of the Bezier curve is equal to the number of control points of the curve.

---
Bezier Curve
Quadratic Bezier Curve
Degree of polynomials = 2
Order (k) = 3
Number of Control points = k = 3
Cubic Bezier Curve
Degree of polynomials = 2
Order (k) = 4
Number of Control points = k = 4

---
Bezier Curve
- Definitions for the Quadratic Bezier Curve
  - The Analytical Formula
  - The Geometric Construction Formula

---
Bezier Curve
- Definitions for the Cubic Bezier Curve
  - The Analytical Formula
  - The Geometric Construction Formula

---
Bezier Curves
- A few traits
  - Has global propogation
    i.e. All the control points are responsible for the curve, changing even one points affects the whole curve
  - The degree of polynomials defining the curve increases as the number of control points increase.

---
Bezier Surfaces
The extension of Bezier curves to surfaces is called the Bezier surface. The surface is constructed from and (n+1)x(m+1) array of control points { Pi,j : 0 <=i<= n, 0<=j<=m }. The following shows a set of control points for m=n=3. There are no restrictions on the location of the control points.

---
Bezier Surfaces
The surface generated by the control points is defined using two variables u and v.
If we set v equal to 0, we obtain the definition for a Bezier Curve.

---
Bezier Surfaces
We observe that for extreme values of u and V, w get Bezier curves for the surface, Hence we can conclude that all the edge curves of the Bezier surface are Bezier Curves. For all P(u,0), P(u,1), P(0,V), P(1,V)
It also implies that the corner points are actually on the patch.

---
Transitioning to B-Spline Curves
- Changing the parameterization of the Bezier curve
  - We’ve seen that the parameter ‘t’ that we used for defining Bezier curves was constrained between 0 and 1. i.e. 0 <= t <= 1
  - But we may need to define the Bezier curve between an arbitrary interval of a and b so that a <= t <= b, for this we need to change our Bernstein polynomials. This can easily be done by using following definition
  - Note that the new polynomials will still make an affine combination

---
Transitioning to B-Spline Curves
- Thus we can define a function τ(t) where
  τ(t) = t-a / b-a and redefine the equation for our curve as.
- We’ve parameterized the equation of the curve to work over the interval [a,b]

---
Continuity of Curves
- Consider the two curves in the example below defined by their own set of control points
  P(t) : {P0,P1,P2,P3} and Q(t):{Q0,Q1,Q2,Q3}.
- Consider t for P(t) lies in the interval [a,b] and t for Q(t) lies in the interval [b,c]. If we were to patch these curves together we’ll need to define another curve R(t) operating over the interval [a,c]
- In order for R(t) to be C0 continuous we’ll need to make sure P3 = Q0, so there are no breaks in the curve.
- In order for the curve to be C1 continuous, we’ll need to make sure the 1st derivatives at P3 and Q0 are same as well. i.e. P3’ = Q0’
- In order for the curve to be C2 continuous, we’ll need to make sure the 2nd derivatives at P3 and Q0 are th same as well i.e P3” = Q0”

---
B-Spline Curves
- For a B-Spline curve we’re given a set of n+1 control points {P0,P1,..,Pn}, the desired order of the curve ‘k’ (This is new!!). And a set of n+k+1 knots {t0,t1,...tn+k}
- We’ll be looking at NURBS, as they are the more popular B-Splines
  *Non Uniform Rational B-Splines

---
B-Spline Curves
Following is how a B-Spline curve is defined geometrically
where
and
ti = 0 if i< k
ti = i-k+1 if k<=i<=n
ti = n-k+2 if i > n

---
B-Spline Curves
Following is how a B-Spline curve is defined analytically

---
What’s a NURBS?
- A B-Spline curve is called as a NURB if the contribution/influence of a control point to the segments of the curve vary.
- But NURBS are the B-Splines that fit the Bezier curve definition.

---
B-Spline Surface
The extension of B-Spline curve to surfaces is called a B-Spline patch. The patch is constructed from an (n+1)x(m+1) array of control points {Pi,j : 0<=i<=n, 0<=j<=m}, an order k and two set of knots {u0,u1, .., un+k} and {v0,v1, .., vm+k}

---
B-Spline Surfaces
- Similar to the Bezier Surface but we change the equations to generate B-Spline curves instead of Bezier curves when fixing either of the u or v parameters.
- Defined by the following equation
- Properties of the B-spline patch are similar to the Bezier patch.
  - All edge curves of the patch are B-spline curves.
  - The patch is contained in the convex hull of the control points.
  - By fixing u, the resulting curve is a B-spline curve on the patch.
  - By fixing v, the resulting curve is a B-spline curve on the patch.